## Slide 1: Machine Real-Time Monitoring System Base On OPC UA
學生:林清河
指導教授:黃士嘉 老師
授課老師:李宗演 老師

## Slide 2: Outline
Introduction
Related Work
System Architecture and Design
Experimental Results
Conclusion
Reference

## Slide 3: Introduction
Assist in Upgrading Industries, Towards Industry 4.0:Smart Manufacturing.
  It’s very difficult to replace the new machine.
  Cost too high.
Collecting Machine Data.
  Add sensor.
  Read the existing information of the machine.
Base on industrial communication standard: OPC UA protocol, develop a system with data collection and monitoring.
  Transfer data to server use wifi or bluetooth.
  Display monitoring data by web and app.

## Slide 4: Introduction(con.)
Implement a monitoring system with cross-platform and unified communication standards.
Arduino as external sensor control.
  Expandability.
  Low-cost.
Break through the limited of factory space.
OPC UA advantage:
  Machine to machine communication protocol.
  Focus on data collection and control.
  Open, Cross-platform, SOA, Robust security.

## Slide 5: Related Work
MT Connect:
  Manufacturing standard.
  Lightweight, Open, Flexible protocol.
  Read-only.
OPC:
  Standards and specifications for industrial telecommunication
  Use in process control and manufacturing automation applications.
  Base on Microsoft.
MT Connect-OPC UA:
  Communicate with each other.
  Including the advantages of both, but it’s difficulties in implementation.

## Slide 6: Related Work(con.)
 | MT Connect | OPC | OPC UA | MT Connect-OPC UA
Transport format | XML | XML、binary | XML、binary | XML、binary
Communication Protocal | HTTP | Web Service、TCP | Web Service、TCP | Web Service、TCP
Complexity | Low | Medium | Medium | High
Security | High | Low | High | High
Write | No | Yes | Yes | Yes
Cross-Platform | Yes | No | Yes | Yes
Interoperability | Low | Low | High | High

## Slide 7: System Architecture and Design
Machine
Machine
OPC UA Server
Windows
I/0
Port
DB Server
Server
API
Sensor
Arduino
OPC UA Client
Web Server
APP
Browser

## Slide 8: Experimental Results
Existing way :
  Only see the current information and historical data cannot be known.
  Unable to monitor instantly.

## Slide 9: Experimental Results
Use OPC UA:
  Real time monitor factory information
  See the history data.
  Show wrong message.
Real-Time Transmission :
  One sensor :12-14 time/s.
  About 280KB each time.
  Total:3.3-3.9Mbps.
  Bluetooth transmission speed:24Mbps.
  Achieves purpose of real time monitor.
Browser
Monitor Screen
Yield
Historical Production Report
Real-Time
Information
APP
Alarm

## Slide 10: Conclusion
Considering the upgrade cost of the machine and the flexibility of the equipment expansion, we propose the "Machine Real-Time Monitoring System Base On OPC UA" .
Design a system to read the sensor and machine information.
Real time display machine information via the web and app.
Need to be customized.
Improve the ability of traditional manufacturing information integration.

## Slide 11: Reference
W. K and M. S, “Standalone OPC UA Wrapper for Industrial Monitoring and Control Systems,” IEEE Access, vol. 6, pp. 36557-36570, Jul. 2018.
B. K. Kim, Y. J. Heo, J. C. Na, “Design of unidirectional security gateway system for secure monitoring of OPC-UA data,” in Proc. ICTC. Korea, Oct. 2017.
S. G, J. P, F. Palm, “RESTful Industrial Communication With OPC UA,” IEEE Transactions on Industrial Informatics, vol. 12, pp. 1832-1841, Feb. 2016.

## Slide 12
Thank you